GOVERNMENT OF TELANGANA

MUNICIPAL ADMINISTRATION DEPARTMENT

From							To

# Dr. B. Janardhan Reddy, IAS			The Municipal Commissioner,

Commissioner & Director of 				__________________ Municipality/

Municipal Administration, 					         Municipal Corporation,

Hyderabad.					       _______________________________

Sir,

Sub:	Preventive Measure for Heavy Rains - Preventive measures, collection and analysis of water samples, remedial measures to be taken to avert water borne diseases, Desiltation of drains etc. - Certain instructions – Regarding.

<<< >>>>

As a measure to pre monsoon /cyclone preparedness, all Municipal Commissioner in Warangal Region & Hyderabad Region shall take up measures to avert water borne diseases apart from instructions being issued from time to time to ensure supply of safe drinking water to public. These measures are classified into three stages viz., Preventive, Monitoring and Remedial which are as follows:

- Preventive Measures to be taken up

- Drinking water storage tanks must be ensured free from contamination.

- All the open drains/storm water drains shall be cleared of silt.

(i)	For quick disposal of sullage/ rain water, clearing of storm water drains 			should be taken up immediately with a suitable action plan to clear off the 			silt before onset of monsoon.

(ii) 	The  silt  removed  from  the  drains  shall  be  taken  away  immediately

after becoming dry avoiding the access again into the drain unlike the 	earlier practice.

- Garbage and debris shall be lifted daily by making necessary arrangements.

- Ensure joints of drinking water pipe lines do not come in drains/ Nalas if necessary by realigning of pipe lines providing suitable casing for water supply pipes to avoid contamination.

- Sufficient contact time with high dosages of chlorine should be maintained in pumping mains and ELSRs to ensure action on the organic matter to eliminate its presence in the treated water.  Display boards indicating dates of cleaning of ELSRs and sumps shall be erected.

- All the distribution lines should be scoured regularly.

- Ensure no pit taps in the town to safeguard against entry of polluted water in to distribution system.

- Leaks in the distribution systems shall be attended on top priority.

- Sleeves shall be provided on the pipe lines crossing drains to avoid direct contact of drain water with water pipe lines.

- No used / waste water is to be allowed to accumulate around the drinking water sources.  Soak pits/ leading drains shall be constructed for all bore wells and Public taps if they are not constructed.

- Platforms for all bore wells and public taps shall be constructed.

- Campaigning shall be done through media/ announcements and mike/ pamphlets for not to throw the waste materials in the drains/ culverts.

- Special attention and care is to be given to the vulnerable places / localities where there is possibility of pollution based on the previous records.

II	Monitoring of Water Quality:

- CRITICAL & PROBLEMATIC AREAS

- A Task Team of officers consisting of the Engineers from Public Health Department, Municipal Officers looking after sanitation and Water Supply and other Public Health officers to be constituted. Team shall identify the critical and problematic areas in the town and shall furnish inspection report every day and the Municipal Commissioner shall indicate the follow up action taken.

ii)   Invariably they should check residual Chlorine in those problematic areas on daily

basis.

They should conduct H2S strip test / bacteriological examination in these areas frequently and should be documented.

- One sample  shall  invariably  be collected  at  source after  post chlorination at

treatment plant/ infiltration gallery/ bore well.

- Samples at the rate 1% of HSCs and 2% of PSPs to be collected in a cycle and analysed for residual chlorine.  The total No. of samples collected for each Municipality is fixed at the rate of one sample for every 5,000 population per day.

- The residual chlorine found should not be less than 0.2 P.P.M. If the same is less than 0.2 P.P.M, reasons for less chlorine content shall be immediately identified, examined and corrective measures shall be taken immediately.

- After rectifying the cause of depletion in the residual chlorine, the water samples need to be collected again and analyzed for residual chlorine and bacteriological analysis by the nearest Indian Preventive Medicine Laboratory duly conducting H2S Strip test to confirm whether it is wholesome or unwholesome. Accordingly corrective measures for rectification of water supply distribution need to be repeated for ascertaining the wholesomeness/portability of water.

- Any untoward incidents occurred, Municipal Commissioner of Hyderabad & Warangal Regions including Corporation Commissioners shall update the status/ATR on cdma website (Telangana).

III 	Remedial Measures:

- Whenever pollution is detected the public in the area shall be advised to use chlorine tablets to maintain residual chlorine in the drinking water stored. Also Public shall be advised to boil water before consumption.

- When ever the pollution is noticed, that area should be isolated duly disconnecting the water supply through distribution network.  Tanker water supply should be resorted until the source of pollution is arrested and water supply is restored.

- Any case of disruption of water supply should be immediately brought to the notice of the Regional officers as well as this office by the Municipal Commissioners/ Municipal Engineers.

- Required water tankers mounted on lorries need to be deployed to ensure that safe drinking water is transported and made available in the localities which are affected with water borne diseases.

- The water tankers should be leak proof and well painted and disinfected regularly cleaned to avoid any possibility of wastage of water during transportation and also   to avoid any sort of possible contamination.

- Wherever Urban Health Centers are there, sufficient stock of medicines must be kept ready to deal with water borne diseases like gastroenteritis, etc.

- Adequate stocks of larvicides must be kept for taking up antilarvel operations after the cyclone in water stagnated areas

- Diesel Engines must be hired and kept at all such places to bail out water as quickly as possible to avoid the submergence of residential localities.

The above instructions shall be scrupulously followed.

Yours faithfully

Sd/-

Commissioner & Director